## Slide 1: Hardware Software Platforms Project Presentation
LED Matrix Control Tutorial
Carlos Ivan Torres Quero
charly_tq@outlook.com
Islam Hammad
Islam.HAMMAD@student.umons.ac.be

## Slide 2: Contents
Context
Software
  Quartus Prime
  Model Sim Altera
Hardware
  LED Matrix
  Max7219 IC
Implementation
  Driver
  Testbench
  Simulation
  Results

## Slide 3: Context
LED Matrix requires 3 signals to be driven:
  DIN
  CS
  CLK
The FPGA must be able to create the control signals of the MAX7419
Final Challenge: Drive the Matrix using the FPGA having the MAX7219 as an intermediate component

## Slide 4: LED Matrix MAX7219
Power Supply: 4.0V ~ 5.5V
Supply Current: 330mA
Segment drive source current -40mA
Scan rate 500-1300Hz (800Hz Typ.)
CLK max 10MHz
Voltage Specs.
Vih (input high) min 3.5V
Vil (input low) max 0.8V
Voh (output high) min V+-1
Vol (output low) max 0.4V

## Slide 5: MAX7219 IC

## Slide 6: Signal
8 bits for the data and 4 for the address to know which LED or line of LED and so on that we want to switch or not.

## Slide 7: Driver
Designing a driver to make the FPGA and the MAX7219 able to communicate each other.
Entity:
Inputs: Clk (frequency for the IC)
16 bits signal
Outputs: CLK (Frequency for the matrix)
CS signal
Data Array signal for matrix
16 States ->
State 1: Recept (Receive the Data Array)
15 States: Counters

## Slide 8: Driver
Variable Donnee receive the data
16 States:
  State 1: Recept (Receive the Data Array)
  15 States: Counters

## Slide 9: Testbench

## Slide 10: Application
  The first 4 bits are never used for this device.
  The last 8 bits each monitor one led in the line.
  If the bits are equal to 1, the corresponding LEDs will be lit and in the same way, they will be off if the bits are equal to 0.

## Slide 11: Useful Links